## Slide 1: BMP280 Sensor communicate with Android Things
Notes: Reference:
https://github.com/androidthings/drivers-samples/tree/master/bmx280
https://github.com/androidthings/contrib-drivers/tree/master/bmx280

## Slide 2: Temperature sensor sample for Android Things
Environment For Raspberry pi 3 Model B
  Devices
    Raspberry pi 3 model B
    BMP 280
  Platform
    Android things
Android Debug Bridge (ADB)
Environment For Desktop
  OS
    Window 10
  Software
    Android Studio
Notes: Peripheral I/O: communication APIs to sensors and actuators
General Purpose Input/Output(GPIO):
  use to read the state of a binary input device and control the on/off state of a binary output device
  Adding permission to manifest file
  Connect port: in order to open connection to a CPIO port you will using unique GPIO port name to open connection.
  Read:
    setDirection() with DIRECTION_IN
    Current state by getValue()
  Close connection: in order to free up resources.
Pulse Width Modulation(PWM): use to control actuators
Serial Communication: use to transfer larger payloads of data between two or more smart devices connected on the same local bus.

## Slide 3: Development of temperature sensor
Start Android Studio
Programming
Connect with Android Things Through ADB(Android Debug Bridge)

## Slide 4: Development of temperature sensor
Start Android Studio
  Start a new Android Studio project
Programming
Connect with Android Things Through ADB(Android Debug Bridge)

## Slide 5: Development of temperature sensor
Start Android Studio
  Start a new Android Studio project
  Set information of Application name, Company domain, Project location
Programming
Connect with Android Things Through ADB(Android Debug Bridge)
Notes: Application name: application`s name
Company domain:
Project location: workspace for your project
Revert your company domain + application name = package name

## Slide 6: Development of temperature sensor
Start Android Studio
  Start a new Android Studio project
  Set information of Application name, Company domain, Project location
  Choose device and Android things version
Programming
Connect with Android Things Through ADB(Android Debug Bridge)

## Slide 7: Development of temperature sensor
Start Android Studio
  Start a new Android Studio project
  Set information of Application name, Company domain, Project location
  Choose device and Android things version
  Add Activity : default
Programming
Connect with Android Things Through ADB(Android Debug Bridge)

## Slide 8: Development of temperature sensor
Start Android Studio
  Start a new Android Studio project
  Set information of Application name, Company domain, Project location
  Choose device and Android things version
  Add Activity : default
  Configure Activity: default
Programming
Connect with Android Things Through ADB(Android Debug Bridge)

## Slide 9: Development of temperature sensor
Start Android Studio
Programming
  Add permission
Connect with Android Things Through ADB(Android Debug Bridge)

## Slide 10: Development of temperature sensor
Start Android Studio
Programming
  Add permission
  Add dependencies
Connect with Android Things Through ADB(Android Debug Bridge)

## Slide 11: Development of temperature sensor
Start Android Studio
Programming
  Add permission
  Add dependencies
  Add code
    Add Class BoardDefaults
Connect with Android Things Through ADB(Android Debug Bridge)
Notes: BoardDefaults class: return alternate functions for each board design

## Slide 12: Development of temperature sensor
Start Android Studio
Programming
  Add permission
  Add dependencies
  Add code
    Add Class BoardDefaults
    Add code in MainActivity
Connect with Android Things Through ADB(Android Debug Bridge)
import android.os.Build; @SuppressWarnings("WeakerAccess") public class BoardDefaults { // The name of the industrial design private static final String DEVICE_RPI3 = "rpi3"; private static final String DEVICE_IMX6UL_PICO = "imx6ul_pico"; private static final String DEVICE_IMX7D_PICO = "imx7d_pico"; /** * Return the preferred I2C port for each board. */ public static String getI2CPort() { switch (Build.DEVICE) { case DEVICE_RPI3: return "I2C1"; case DEVICE_IMX6UL_PICO: return "I2C2"; case DEVICE_IMX7D_PICO: return "I2C1"; default: throw new IllegalStateException("Unknown Build.DEVICE " + Build.DEVICE); } } }
Notes: Annotations: allow us to add metadata information into out source code but not affect the execution of the program). Begin with JDK 5.
Instructions to the compiler: there are three built-in annotations available in java(@ Deprecated, @Override, @SuppressWarnings) that can bu used for giving certain instructions to the compiler.
  SuppressWarnings: instructs compiler to ignore specific warnings.
Compile-time instructors: Annotations can provide compile-time instructions to the compiler that can be further used by software build tools for generating code, XML files etc.
Runtime instructions: we can define annotations to be available at runtime which we can access using java reflection and can be used to give instructions to the program at runtime.
Annotations can be applied to the classes, interfaces, methods and fields.

## Slide 13: Development of temperature sensor
Start Android Studio
Programming
  Add permission
  Add dependencies
  Add code
    Add Class BoardDefaults
    Add code in MainActivity
Connect with Android Things Through ADB(Android Debug Bridge)
private static final String TAG = "Android sensor test"; private Bmx280 mBmx280; @Override protected void onCreate(Bundle savedInstanceState) { super.onCreate(savedInstanceState); setContentView(R.layout.activity_main); try {
// make instance for BMP driver mBmx280 = new Bmx280(BoardDefaults.getI2CPort()); // Configure driver settings according to your use case mBmx280.setTemperatureOversampling(Bmx280.OVERSAMPLING_1X); mBmx280.setMode(Bmx280.MODE_NORMAL); //wake up sensor Log.i(TAG,"connect with sensor"); } catch (IOException e) { } new Thread(new Runnable() { //make thread for period read temperature public void run() { while (true) { try { Log.i(TAG, "start thread"); Thread.sleep(1000); float temperature = mBmx280.readTemperature(); Log.i(TAG, String.valueOf(temperature)); } catch (IOException e) { // error reading temperature } catch (InterruptedException e) { e.printStackTrace(); } } }).start(); }

## Slide 14: Development of temperature sensor
Start Android Studio
Programming
  Add permission
  Add dependencies
  Add code
    Add Class BoardDefaults
    Add code in MainActivity
Connect with Android Things Through ADB(Android Debug Bridge)
@Override protected void onDestroy() { super.onDestroy(); Log.i(TAG, “disconnect with sensor"); if (mBmx280 != null) { try { mBmx280.setMode(Bmx280.MODE_SLEEP); mBmx280.close(); } catch (IOException e) { // error closing sensor } } }

## Slide 15: Development of temperature sensor
Start Android Studio
Programming
Connect with Android Things Through ADB(Android Debug Bridge)
  Start terminal
Notes: Problem
adb is not recognized as an internal or external command
Resolution
set environment variable to path
  Click start
  Type edit environment variables for your account
  Double Click path
  Click new
  Paste that path in
adb tool is located in C:\Users\[your user name]\AppData\Local\Android\sdk\platform-tools by default

## Slide 16: Development of temperature sensor
Start Android Studio
Programming
Connect with Android Things Through ADB(Android Debug Bridge)
  Start terminal
  connect with device through adb
    IP for device
    Port 5555 default

## Slide 17: Development of temperature sensor
Start Android Studio
Programming
Connect with Android Things Through ADB(Android Debug Bridge)
Execute Application

## Slide 18: Development of temperature sensor
Start Android Studio
Programming
Connect with Android Things Through ADB(Android Debug Bridge)
Execute Application

## Slide 19: Reference
https://github.com/androidthings/drivers-samples/tree/master/bmx280
https://github.com/androidthings/contrib-drivers/tree/master/bmx280
http://www.robot-electronics.co.uk/i2c-tutorial
https://beginnersbook.com/2014/09/java-annotations/