## Slide 1: Environment Set UP for BMP280 Sensor with Android Things
Notes: Reference:
https://github.com/androidthings/drivers-samples/tree/master/bmx280
https://github.com/androidthings/contrib-drivers/tree/master/bmx280

## Slide 2: Environments
Environment For Raspberry pi 3 Model B
  Devices
    Raspberry pi 3 model B
    BMP 280
  Platform
    Android things
Android Debug Bridge (ADB)
Environment For Desktop
  OS
    Window 10
  Software
    Android Studio
Notes: Peripheral I/O: communication APIs to sensors and actuators
General Purpose Input/Output(GPIO):
  use to read the state of a binary input device and control the on/off state of a binary output device
  Adding permission to manifest file
  Connect port: in order to open connection to a CPIO port you will using unique GPIO port name to open connection.
  Read:
    setDirection() with DIRECTION_IN
    Current state by getValue()
  Close connection: in order to free up resources.
Pulse Width Modulation(PWM): use to control actuators
Serial Communication: use to transfer larger payloads of data between two or more smart devices connected on the same local bus.

## Slide 3: Environment for Development
Requirement
  JDK 8
Android Studio install

## Slide 4: Environment for Development
JDK 8 install
  Download: https://www.oracle.com/technetwork/java/javase/downloads/index.html
  Execute downloaded file
  Set java environment variable
1
2
3

## Slide 5: Environment for Development
JDK 8 install
  Download: https://www.oracle.com/technetwork/java/javase/downloads/index.html
  Execute downloaded file
    Download JDK
    Download JRE
  Set java environment variable

## Slide 6: Environment for Development
JDK 8 install
  Download: https://www.oracle.com/technetwork/java/javase/downloads/index.html
  Execute downloaded file
    Download JDK
    Download JRE
  Set java environment variable
    Copy JDK folder location
    Open environment variables window
    Set JAVA_HOME
1
2

## Slide 7: Environment for Development
JDK 8 install
  Download: https://www.oracle.com/technetwork/java/javase/downloads/index.html
  Execute downloaded file
    Download JDK
    Download JRE
  Set java environment variable
    Copy JDK folder location
    Open environment variables window
      On this PC click right mouse
    Set JAVA_HOME
1
2
3

## Slide 8: Environment for Development
JDK 8 install
  Download: https://www.oracle.com/technetwork/java/javase/downloads/index.html
  Execute downloaded file
    Download JDK
    Download JRE
  Set java environment variable
    Copy JDK folder location
    Open environment variables window
    Set JAVA_HOME

## Slide 9: Environment for Development
JDK 8 install
  Download: https://www.oracle.com/technetwork/java/javase/downloads/index.html
  Execute downloaded file
    Download JDK
    Download JRE
  Set java environment variable
    Copy JDK folder location
    Open environment variables window
    Set JAVA_HOME

## Slide 10: Environment for Development
JDK 8 install
  Download: https://www.oracle.com/technetwork/java/javase/downloads/index.html
  Execute downloaded file
    Download JDK
    Download JRE
  Set java environment variable
    Copy JDK folder location
    Open environment variables window
    Set JAVA_HOME
    Set Path
1
2
3

## Slide 11: Environment for Development
JDK 8 install
  Download: https://www.oracle.com/technetwork/java/javase/downloads/index.html
  Execute downloaded file
    Download JDK
    Download JRE
  Set java environment variable
    Copy JDK folder location
    Open environment variables window
    Set JAVA_HOME
    Set Path
1
2
3

## Slide 12: Environment for Development
JDK 8 install
  Verify
1
2
3

## Slide 13: Environment for Development
Android Studio install
  Download exe installer
  Execute exe file

## Slide 14: Environment for Development
Android Studio install
  Download exe installer
  Execute exe file

## Slide 15: Environment for Development
Android Studio install
  Download zip file
    Select download options
    Choose one that suit with your environment
  Unzip downloaded file

## Slide 16: Environment for Raspberry Pi 3 Model B
Android Things: IoT operating system which derived form Android.
Let you develop apps for your devices with existing android development tools, APIs, and resources.
Flashing android things image to device
required
  Android Things Setup Utility or Win32diskImage
  microSD card larger than 8GB
MicroSD Card
MicroSD Card Reader

## Slide 17: Environment for Raspberry Pi 3 Model B
Using Utility
  Download and Unzip : https://partner.android.com/things/console#/tools
    Unzip
  Execute Tool
  Write AndroidThings to Micro Card
    Select actions
    Select hardware
    Select image
    Select Micro SD card to install take several minutes
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 18: Environment for Raspberry Pi 3 Model B
Using Utility
  Download and Unzip
  Execute Tool
    Connect Micro Card Reader with Computer
    Run as administrator
  Write AndroidThings to Micro Card
    Select actions
    Select hardware
    Select image
    Select Micro SD card to install take several minutes
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 19: Environment for Raspberry Pi 3 Model B
Using Utility
  Download and Unzip
  Execute Tool
  Write AndroidThings to Micro Card
    Select actions
    Select hardware
    Select image
    Select Micro SD card to install take several minutes
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 20: Environment for Raspberry Pi 3 Model B
Using Utility
  Verify
    Connect Raspberry Pi with Peripherals(mouse, keyboard, monitor, power, SD Card, Ethernet Cable)
USB Port
Ethernet port
HDMI port
Power
Micro SD Card
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 21: Environment for Raspberry Pi 3 Model B
Using Utility
  Verify
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 22: Environment for Raspberry Pi 3 Model B
Using Win32diskImage
  Download Win32diskImage
  Download image of android things
  Write Image to Micro SD card
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 23: Environment for Raspberry Pi 3 Model B
Using Win32diskImage
  Download Win32diskImage
    https://sourceforge.net/projects/win32diskimager/
  Download image of android things
  Write Image to Micro SD card
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 24: Environment for Raspberry Pi 3 Model B
Using Win32diskImage
  Download Win32diskImage
  Download image of android things
    Create an Android Things product
    Create device build
    Download Image
  Write Image to Micro SD card
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 25: Environment for Raspberry Pi 3 Model B
Using Win32diskImage
  Download Win32diskImage
  Download image of android things
    Create an Android Things product
    Create device build
    Download Image
  Write Image to Micro SD card
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 26: Environment for Raspberry Pi 3 Model B
Using Win32diskImage
  Download Win32diskImage
  Download image of android things
    Create an Android Things product
    Create device build
    Download Image
  Write Image to Micro SD card
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 27: Environment for Raspberry Pi 3 Model B
Using Win32diskImage
  Download Win32diskImage
  Download image of android things
    Create an Android Things product
    Create device build
    Download Image
  Write Image to Micro SD card
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 28: Environment for Raspberry Pi 3 Model B
Using Win32diskImage
  Download Win32diskImage
  Download image of android things
    Create an Android Things product
    Create device build
    Download Image
  Write Image to Micro SD card
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 29: Environment for Raspberry Pi 3 Model B
Using Win32diskImage
  Download Win32diskImage
  Download image of android things
    Create an Android Things product
    Create device build
    Download Image
  Write Image to Micro SD card
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 30: Environment for Raspberry Pi 3 Model B
Using Win32diskImage
  Download Win32diskImage
  Download image of android things
    Create an Android Things product
    Create device build
    Download Image
  Write Image to Micro SD card
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 31: Environment for Raspberry Pi 3 Model B
Using Win32diskImage
  Download Win32diskImage
  Download image of android things
    Create an Android Things product
    Create device build
    Download Image
  Write Image to Micro SD card
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 32: Environment for Raspberry Pi 3 Model B
Using Win32diskImage
  Download Win32diskImage
  Download image of android things
    Create an Android Things product
    Create device build
    Download Image
  Write Image to Micro SD card
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 33: Environment for Raspberry Pi 3 Model B
Using Win32diskImage
  Download Win32diskImage
  Download image of android things
    Create an Android Things product
    Create device build
    Download Image
  Write Image to Micro SD card
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 34: Environment for Raspberry Pi 3 Model B
Using Win32diskImage
  Download Win32diskImage
  Download image of android things
    Create an Android Things product
    Create device build
    Download Image
  Write Image to Micro SD card
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 35: Environment for Raspberry Pi 3 Model B
Using Win32diskImage
  Download Win32diskImage
  Download image of android things
    Create an Android Things product
    Create device build
    Download Image
  Write Image to Micro SD card
    Run Win32diskImage
    Select image
    Select SD card device
    write it for SD card
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 36: Environment for Raspberry Pi 3 Model B
Using Win32diskImage
  Download Win32diskImage
  Download image of android things
    Create an Android Things product
    Create device build
    Download Image
  Write Image to Micro SD card
    Run Win32diskImage
    Select image
    Select SD card device
    write it for SD card
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 37: Environment for Raspberry Pi 3 Model B
Using Win32diskImage
  Download Win32diskImage
  Download image of android things
    Create an Android Things product
    Create device build
    Download Image
  Write Image to Micro SD card
    Run Win32diskImage
    Select image
    Select SD card device
    write it for SD card
Notes: Android Things Console: Can push your own app updates to devices using the Android Things Console.
Provides tools to install and update the system image on supported hardware devices. This allows you to push updates to users, test deployments on your own hardware.
  Prerequisite: google account
  Create an Android Things Product
  Configure Product
    Add models: you can use models to create variants of application builds that all run on the same underlying hardware
    Change product settings
    Share products with other console users
  Create a device build
    Name build configuration
    Select Android Things version
    Select applications you developed or google serviced
    Add additional build resources
    Edit hardware configurations: allow you to define peripherals and configure their attributes
    Edit partition size
Adb tool location hidden use terminal cd to there
C:\Users\youngwook\AppData\Local\Android\Sdk\platform-tools> adb connect <ip-address> or adb connect android.local

## Slide 38: Environment for Raspberry Pi 3 Model B set BMP280
BMP280
  Sensor for temperature and barometric pressure
  Use with 3v or 5v logic microcontroller
  Pins
    Power Pins:
      Vin: power pin
      3v3: 3.3 V output from voltage regulator
      GND: common ground for poser and logic
    I2C Logic pins:
      SCL: I2C clock pin
      SDA: I2c data pin
Notes: I2C(Inter Integrated Circuit communications)
  Communication protocol for electronic parts
VDC(Volts Direct Current)

## Slide 39: Environment for Raspberry Pi 3 Model B set BMP280 Schematics
Schematics: connection between raspberry pi and BMP280
Pins
  Vin: pin number 2 of RaspBerry pi 3
  GND: pin number 9 of RaspBerry pi 3
  SCL: pin number 3 of RaspBerry pi 3
  SDA: pin number 5 of RaspBerry pi 3

## Slide 40: Reference
http://www.automationtestinghub.com/setup-java-environment-variables/
http://www.automationtestinghub.com/download-and-install-java/
https://github.com/androidthings/drivers-samples/tree/master/bmx280
https://github.com/androidthings/contrib-drivers/tree/master/bmx280